## Slide 1: GranaSat Batteries Tester
Blanca Cano Camarero
Miguel Romero García

## Slide 2: Index
Planning………………………………………………………………………………………….3
Tests.………………………………………………………………………………………………4
Equipent used…………………………………………………………………………………5
Multimeter control software…………………………………………………………..6
Interface evolution…………………………………………………………………………7
Python libreries in a virtual enviroment………………………………………….8

## Slide 3: Planning
We will test batteries in some different situations. First, in the picture we can see the lithium ion battery model, which has a voltage source that charge the battery, and at the end, the points where you connect the load in order to discharge the battery
INTERFACE
Blanca will made the interface of the program for control the batteries and the different tests.
TEST
Miguel will made the code for control the differents equipments to use in the test
TEST
We will made the differents test using the equipment like the vacuum chamber
SOFTWARE
HARDWARE

## Slide 4: Test #1: High Vacuum Test
Battery capacity
Battery loss percentage after vacuum
Change in size after vacuum test
Test #2: Capacity and Internal Resistance vs Temperature
Battery capacity versus temperature
Battery internal resistance versus temperature
Charging/ discharging voltage and current curves at different temperatures.
Battery size in charged and uncharged state
C → Measure of the rate at which a battery is discharged relative to its maximum capaity
Test #3: Self-Discharge Test
Battery loss of energy over long periods.
Test #4: LEO Cycling
Battery degradation over continuous charge/discharge periods at border temperatures.
Battery charge/ discharge curve degradation.
Test #5: EMF vs SOC
Battery curve of the electromotive force versus the state of charge
Test #6-7: Reduced pressure 30 %/80% DOD Cycling
Evolution of EODV (End of Discharge Voltage) versus degradation.
Evolution of the battery capacity and efficiency versus degradation

## Slide 5: Equiptment Used
E3631A DC-Supply
6063B DC-Load
Multimeter SDM3065X
The triple output supply offers three independent outputs: 0 to 6 V/5A, 0 to +25V/1A and 0 to –25V/1A. The 6 V output is electrically isolated from the ±25 V supply to minimize any interference between circuits under test. The ±25 V outputs can be set to track each other.
Current: 0 to 10 A
Volts: 3 to 240 V
Maximum power: 250 W
The multimeter read the voltage and current of the battery, and we use it because the 6063B DC-Load hasn’t got the same precision as the multimeter

## Slide 6
Multimeter control, software
Instrument comprobation
And value setting
Create our own class in python using visa libraries.
PLC value setting
PLC value reading
Current
voltage
MEAS::CURR
Reconfigure all instrument
Problems
Solutions
Create our own funtion of measure.
PLC
Average in time of
Current
Capacity
Work at 60hz

## Slide 7: Interface evolution
First approach
Make contact dash libray
Two decimal precision
ACTUAL APPROACH
Two graphics to measure current, voltage and capacity.
Posicionate moise over the graphic to know exactly data.
Posibility to export to png, pdf…
Zoom in, zoom aut
Next implementation
Interactive visualization
Include checkboxes
Include buttons

## Slide 8: Python libraries in a virtual environment
Installation
python3 -m pipenv shell
Libraries
Dash create our own server
Pandas: work with data
Plotly: graphic design
Utilities
Design proyect
Select test type
Charge.csv data sheet
View result in real time
Stablish multimeter comunication
And control it
Error management

## Slide 9
That is all
HAVE YOU ANY QUERY?